# 3D Printing Failure
Part ID/Filename
Distance between A and B on the template
Distance between B and C on the template
Failure type
Printer model
Slicer used

Nozzle diameter, mm
Layer height, mm
Initial layer height, mm
Line width, mm
Infill line width, mm
Top/Bottom pattern, type
Top/Bottom thickness, mm
Infill pattern, type
Infill density, %
Support pattern, type
Support density, %

Printing temperature, ⁰C
Material flow rate, %
Retraction distance, mm
Retraction speed, mm/s
Infill speed, mm/s
Outer wall speed, mm/s
Inner wall speed, mm/s
Support speed, mm/s
Travel speed, mm/s
Fan speed, %

Error height (at what height your print began to fail), mm
Error height (at what layer your print began to fail), layer number
Camera model (it will help us to retrieve the image distortions caused by your camera)

# Firmware Coefficients
For Franklin
u (switch position), mm	v (switch position), mm	w (switch position), mm	e (coupling), steps/mm	Extrusion, %	Feedrate, %	Max travel speed, mm/s