#ifndef CONFIGURATION_H
#define CONFIGURATION_H

/*
 * This is the configuration file for the RepRap Motherboard microcontroller.
 * Set values in it to match your RepRap machine.
 *
 * Lines in here with a
 *
 * // *RO
 *
 * Comment at the end (read-only) should probably only be changed if you really
 * know what you are doing...
 */

// Here are the Motherboard codes; set MOTHERBOARD to the right one
// A standard Mendel is MOTHERBOARD 2

// (Arduino: 0 - no longer in use)
// Sanguino or RepRap Motherboard with direct drive extruders: 1
// RepRap Motherboard with RS485 extruders: 2
// Arduino Mega: 3

#define MOTHERBOARD 2 //cb this is fine

//*********************************************************************************************

// These settings are mainly for Darwin //cb this is not our board, dont change anything in this group

#if MOTHERBOARD == 1

// Comment out this if you are using a thermocouple
#define USE_THERMISTOR

// Set to 1 if enable pins are inverting
// For RepRap stepper boards version 1.x the enable pins are *not* inverting.
// For RepRap stepper boards version 2.x and above the enable pins are inverting.
#define INVERT_ENABLE_PINS 0

// Set to one if the axis opto-sensor outputs inverting (ie: 1 means open, 0 means closed)
// RepRap opto endstops with H21LOI sensors are not inverting; ones with H21LOB
// are inverting.

#define X_ENDSTOP_INVERTING false
#define Y_ENDSTOP_INVERTING false
#define Z_ENDSTOP_INVERTING false

#endif

//**********************************************************************************************

// These settings are mainly for a standard Mendel

#if MOTHERBOARD == 2

// Comment out the next line if you are running a Darwin with a MOTHERBOARD > 1

#define MENDEL 1 // cb leave this uncommented, we arent running a Darwin

// Set to 1 if enable pins are inverting
// For RepRap stepper boards version 1.x the enable pins are *not* inverting.
// For RepRap stepper boards version 2.x and above the enable pins are inverting.
#define INVERT_ENABLE_PINS 1 // cb check stepper board version with makerbot

// Set to one if the axis opto-sensor outputs inverting (ie: 1 means open, 0 means closed)
// RepRap opto endstops with H21LOI sensors are not inverting; ones with H21LOB
// are inverting.

#define X_ENDSTOP_INVERTING true // cb check opto board with makerbot
#define Y_ENDSTOP_INVERTING true
#define Z_ENDSTOP_INVERTING true

// Does your machine have the older standard slotted pullyes (needing lots of motor shaft filing)
// or the newer pulleys with grub screws? Uncomment one of the two next lines.
//#define SLOTTED_PULLEYS
#define GRUB_PULLEYS // cb we wont know this till we are done printing, or we plan which ones to build

#define MY_NAME 'H' // Byte representing the name of this device // cb these seem fine
#define E0_NAME '0' // Byte representing the name of extruder 0
#define E1_NAME '1' // Byte representing the name of extruder 1

#define RS485_MASTER 1 // *RO

#endif

//**********************************************************************************************

// These settings are mainly for a Mendel with an Arduino Mega controller

#if MOTHERBOARD == 3

#define MENDEL 1

// Comment out this if you are using a thermocouple
#define USE_THERMISTOR

// Set to 1 if enable pins are inverting
// For RepRap stepper boards version 1.x the enable pins are *not* inverting.
// For RepRap stepper boards version 2.x and above the enable pins are inverting.
#define INVERT_ENABLE_PINS 1

// Set to one if the axis opto-sensor outputs inverting (ie: 1 means open, 0 means closed)
// RepRap opto endstops with H21LOI sensors are not inverting; ones with H21LOB
// are inverting.

#define X_ENDSTOP_INVERTING true
#define Y_ENDSTOP_INVERTING true
#define Z_ENDSTOP_INVERTING true

// Does your machine have the older standard slotted pullyes (needing lots of motor shaft filing)
// or the newer pulleys with grub screws? Uncomment one of the two next lines.
//#define SLOTTED_PULLEYS
#define GRUB_PULLEYS

#endif

//**********************************************************************************************

// The speed at which to talk with the host computer; default is 19200

#define HOST_BAUD 19200 // *RO

// The number of real extruders

#define EXTRUDER_COUNT 1 // cb changed to 1 from default 2

// Set 1s where you have endstops; 0s where you don't
// Both Darwin and Mendel have MIN endstops, but not MAX ones.

#define ENDSTOPS_MIN_ENABLED 1 //cb these are fine
#define ENDSTOPS_MAX_ENABLED 0

// The width of Henry VIII's thumb (or something).

#define INCHES_TO_MM 25.4 // *RO

// The number of mm below which distances are insignificant (one tenth the
// resolution of the machine is the default value).

#define SMALL_DISTANCE 0.01 // *RO

// Useful to have its square

#define SMALL_DISTANCE2 (SMALL_DISTANCE*SMALL_DISTANCE) // *RO

#ifdef MENDEL

#ifdef SLOTTED_PULLEYS
// define the XYZ parameters of Mendel - standard pulleys

//cb this is probably fine, unless we later notice warping in one dimension, we can change it in the software here
#define X_STEPS_PER_MM 10.047
#define X_STEPS_PER_INCH (X_STEPS_PER_MM*INCHES_TO_MM) // *RO
#define INVERT_X_DIR 0

#define Y_STEPS_PER_MM 10.047
#define Y_STEPS_PER_INCH (Y_STEPS_PER_MM*INCHES_TO_MM) // *RO
#define INVERT_Y_DIR 0

#define Z_STEPS_PER_MM 833.398
#define Z_STEPS_PER_INCH (Z_STEPS_PER_MM*INCHES_TO_MM) // *RO
#define INVERT_Z_DIR 0
#endif

#ifdef GRUB_PULLEYS
// define the XYZ parameters of Mendel - grub-screw pulleys

//cb this is probably fine, unless we later notice warping in one dimension, we can change it in the software here
#define X_STEPS_PER_MM 10.047
#define X_STEPS_PER_INCH (X_STEPS_PER_MM*INCHES_TO_MM) // *RO
#define INVERT_X_DIR 0

#define Y_STEPS_PER_MM 10.047
#define Y_STEPS_PER_INCH (Y_STEPS_PER_MM*INCHES_TO_MM) // *RO
#define INVERT_Y_DIR 0

#define Z_STEPS_PER_MM 833.398
#define Z_STEPS_PER_INCH (Z_STEPS_PER_MM*INCHES_TO_MM) // *RO
#define INVERT_Z_DIR 0
#endif

#endif

#if MOTHERBOARD == 1

// This is for Darwin.

#define X_STEPS_PER_MM 7.99735
#define X_STEPS_PER_INCH (X_STEPS_PER_MM*INCHES_TO_MM) // *RO
#define INVERT_X_DIR 0

#define Y_STEPS_PER_MM 7.99735
#define Y_STEPS_PER_INCH (Y_STEPS_PER_MM*INCHES_TO_MM) // *RO
#define INVERT_Y_DIR 0

#define Z_STEPS_PER_MM 320
#define Z_STEPS_PER_INCH (Z_STEPS_PER_MM*INCHES_TO_MM) // *RO
#define INVERT_Z_DIR 0

#endif

// For when we have a stepper-driven extruder
// E_STEPS_PER_MM is the number of steps needed to
// extrude 1mm out of the nozzle. E0 for extruder 0;
// E1 for extruder 1, and so on.

//#define E_STEPS_PER_MM 0.9 //0.706 // NEMA 17 extruder 5mm diameter drive - empirically adjusted

//#define E_STEPS_PER_MM 2.2 // NEMA 14 geared extruder 8mm diameter drive
#define E0_STEPS_PER_MM 2.0 // NEMA 17 55/11 geared extruder 8mm diameter drive //cb we need to change this line to calibrate our extruder - what motor do we have?
#define E1_STEPS_PER_MM 2.0 // NEMA 17 55/11 geared extruder 8mm diameter drive

//#define E0_STEPS_PER_INCH (E_STEPS_PER_MM*INCHES_TO_MM) // *RO

//our maximum feedrates
#define FAST_XY_FEEDRATE 3000.0 //cb change these later if machine is moving too fast
#define FAST_Z_FEEDRATE 50.0

// Data for acceleration calculations
// Comment out the next line to turn accelerations off
#define ACCELERATION_ON // cb leave this alone, acceleration is good to have
#define SLOW_XY_FEEDRATE 1000.0 // Speed from which to start accelerating //cb this is the threshold speed after which we accelerate
#define SLOW_Z_FEEDRATE 20

#if INVERT_ENABLE_PINS == 1 // *RO
#define ENABLE_ON LOW // *RO
#else // *RO
#define ENABLE_ON HIGH // *RO
#endif // *RO

// Set these to 1 to disable an axis when it's not being used,
// and for the extruder. Usually only Z is disabled when not in
// use. You will probably find that disabling the others (i.e.
// powering down the steppers that drive them) when the ends of
// movements are reached causes poor-quality builds. (Inertia
// causes overshoot if the motors are not left powered up.)

#define DISABLE_X 0
#define DISABLE_Y 0
#define DISABLE_Z 1
#define DISABLE_E 0

// The number of 5-second intervals to wait at the target temperature for things to stabilise.
// Too short, and the extruder will jam as only part of it will be hot enough.
// Too long and the melt will extend too far up the insulating tube.
// Default value: 10

#define WAIT_AT_TEMPERATURE 10

//our command string length

#define COMMAND_SIZE 128 // *RO

// The size of the movement buffer

#define BUFFER_SIZE 4 // *RO

// Number of microseconds between timer interrupts when no movement
// is happening

#define DEFAULT_TICK (long)1000 // *RO

// What delay() value to use when waiting for things to free up in milliseconds

#define WAITING_DELAY 1 // *RO

//******************************************************************************

// You probably only want to edit things below this line if you really really
// know what you are doing...

extern char debugstring[];

void delayMicrosecondsInterruptible(unsigned int us);

// Inline interrupt control functions

inline void enableTimerInterrupt()
{
   TIMSK1 |= (1<<OCIE1A);
}

inline void disableTimerInterrupt()
{
     TIMSK1 &= ~(1<<OCIE1A);
}

inline void setTimerCeiling(unsigned int c)
{
    OCR1A = c;
}

inline void resetTimer()
{
  TCNT2 = 0;
}

#endif

//*************************************************************************

#if 0
// Green machine:
//#define ENDSTOPS_INVERTING 0

// parameters for the Bath U. mendel prototype
#define X_STEPS_PER_MM 13.333333
#define X_STEPS_PER_INCH (X_STEPS_PER_MM*INCHES_TO_MM)
#define INVERT_X_DIR 0

#define Y_STEPS_PER_MM 13.333333
#define Y_STEPS_PER_INCH (Y_STEPS_PER_MM*INCHES_TO_MM)
#define INVERT_Y_DIR 0

// Green machine:
#define Z_STEPS_PER_MM 944.88
// Fat Z cog machine:
//#define Z_STEPS_PER_MM 558.864
// Standard Mendel:
//#define Z_STEPS_PER_MM 833.398
#define Z_STEPS_PER_INCH (Z_STEPS_PER_MM*INCHES_TO_MM)
#define INVERT_Z_DIR 0

#endif